## Slide 1
Erasmus+ Program 2024 Cooperation partnerships in higher education - 2024-1-ES01-KA220-HED-000246733
Student-centered learning for ENVIronmental sustainability at Higher Education Institutions
Measurement Systems and Sustainability
Project Title: Experimental identification of resonance frequency in a Mechanical structure​
Meeting on May 21st.: Initial Project Concept
Team name:
Vibe Finders
Team members:
Patryk Januś Natalia Szymeczko
Patryk Reiter
Szymon Korzuch

## Slide 2
Activity: Topic Analysis
What is the real problem? Time for students: 45 min
Describe the engineering problem:
In reality, mechanical elements and structures experience dynamic loads and vibrations from rotating equipment, impacts, or operational conditions. When these external forces excite a structure near its natural frequency, a phenomenon known as resonance occurs, leading to dramatically increased vibration amplitudes. This is a severe engineering problem because high-amplitude vibrations cause intense noise, structural fatigue, and eventual mechanical failure or equipment damage. Diagnostic and design engineers are directly affected, as unmitigated resonance reduces system reliability, compromises safety, and results in costly operational downtime and premature material waste.
Example questions:
What happens in reality?
Why is this a problem?
Who is affected?
What are the consequences?

## Slide 3
Importance of the Problem Time for students: included in 45 min block
Technical importance
Uncontrolled resonance dramatically amplifies mechanical stress on structural elements. This leads to accelerated material fatigue, crack propagation, and sudden structural failures.
Economic importance
Structural failures from resonance result in high economic losses due to unexpected machinery downtime, emergency repairs, and the need for early replacement of expensive components.
Environmental / sustainability importance
Frequent mechanical breakdowns and component destruction lead to premature disposal of materials, significantly increasing resource consumption and waste generation. Furthermore, resonance causes excessive acoustic pollution (noise) and wastes kinetic energy. By identifying and mitigating resonance, we extend equipment lifespans and reduce the environmental footprint of manufacturing and operating materials.

## Slide 4
Project Challenge Time for students: included in 45 min block
Main engineering question:
How can an integrated data acquisition system, precise IEPE accelerometers, and signal processing algorithms be utilized to accurately identify structural resonance frequencies and assess damping characteristics across different physical configurations to prevent catastrophic fatigue failure?
Expected project outcome:
The expected outcome is a fully functional, automated vibration measurement and diagnostic station. It will feature a calibrated sensor configuration, a web dashboard displaying Fast Fourier Transform (FFT) spectra, time domain signals, structured TDMS logging protocol for raw experimental data, and a persistent SQLite database tracking dominant peak frequencies and decay rates across structural modifications to provide actionable engineering choices.

## Slide 5
Activity: Problem Analysis
Measurement Requirements Time for students: 60 min
Physical quantities to measure:
☐ Temperature X Vibration ☐ Flow ☐ Voltage ☐ Current ☐ Pressure ☐ Other: __________
Why are these measurements important?
Real-world components often differ from theoretical models due to material defects and mounting variations. Measuring actual acceleration allows us to accurately locate the exact resonance frequencies.
Expected measurement conditions:
Measurement duration: 0.5-1 s per impact test
Sampling rate: 5kS/s
Number of channels: 1-2

## Slide 6
Sensor Selection Time for students: included in 60 min block
Sensor | Purpose | Why selected? | Expected range | Expected accuracy | Potential dificulties
PCB-601A02 ICP Accelerometer | measure the dynamic acceleration response of the beam over time after an impact excitation. | It features a high frequency response, integrated electronics, low noise, compatible with our NI-9232/NI-9234 DAQ hardware. | +-50g 0.5-10000 Hz | Sensitivity accuracy: ±10% Non-linearity error: ≤1% Transverse sensitivity: ≤ 5% | Mounting of the sensor to the chassis made of aluminum

## Slide 7
DAQ and LabVIEW Concept Time for students: included in 60 min block
Proposed DAQ configuration:
We will use the NI-9232 IEPE dynamic signal acquisition module inserted into an NI-9171 single-slot USB chassis. The PCB Model 601A02 accelerometer will connect via a coaxial cable directly to Channel 0. In the C# backend, DAQmx tasks will be configured for continuous Analog Input, specifying an IEPE excitation current (typically 2 - 20 mA) to power the sensor's internal amplifier, with a sample rate of 5000 Hz.
Planned software functions:
-Real-time result display -Raw data logging -Signal analysis -FFT analysis -RMS calculations
Initial software concept:
The system utilizes a custom C# backend architecture managing a continuous high-speed DAQmx measurement task. Rather than saving everything, the backend continuously buffers incoming data and monitors the sample stream for a threshold-based trigger event indicating a physical strike. Once triggered, it extracts a precise waveform snapshot capturing a user-defined pre-trigger and post-trigger time window. This transient impact response is saved to a local TDMS file using NI TDMS .NET libraries. Key metrics (like calculated FFT peak resonance and damping characteristics) are written to a local SQLite database, which is immediately pushed to a web frontend application for real-time visualization and system configuration.

## Slide 8
Preliminary System Architecture Time for students: included in 60 min block
Block Diagram
Short explanation of system operation:
The system operates by continuously buffering analog vibration data in a C# backend until a physical strike triggers a precise pre- and post-trigger snapshot. The raw wave data is permanently saved to an TDMS file, while calculated results (such as FFT peak frequencies) and user configurations are logged into an Excel file. To tie everything together, an SQLite database acts as a master registry, storing experimental metadata alongside the absolute file locations of the generated TDMS and Excel reports. Finally, a web frontend queries this SQLite registry to locate the files, extract the data, and visualize the structural performance charts.

## Slide 9
Initial Experimental Setup Time for students: included in 60 min block
Describe the planned experiment:
The experiment involves exciting a mechanical structure (CNC machine) using a hammer strike to trigger continuous vibration data collection. The system will record the physical decay waveform over a specified pre- and post-trigger time window. A Fast Fourier Transform (FFT) algorithm will then convert this snapshot into the frequency domain to identify the exact structural resonance frequencies, and allow for further analysis
Measurement location/environment:
Labolatory Classroom – CNC machine chasis
Planned experimental scenarios:
- Hammer impact response for different structure configurations - Vibration measurement during spindle operation for different structure configurations

## Slide 10
Sustainability Context Time for students: included in 60 min block
How can this project improve sustainability?
☐ Reduce energy consumption ☐ Reduce water consumption x Extend equipment lifetime x Reduce waste ☐ Improve efficiency x Reduce failures/losses
Expected environmental benefits:
By precisely mapping structural resonance frequencies, we can modify physical designs or implement targeted damping solutions to eliminate high-amplitude vibrations, or for example determine the spindle RPM values, which should be avoided during operation. This directly prevents premature material fatigue, dramatically extending the operating lifetime of industrial machinery and components. Consequently, this lowers the raw material footprint, minimizes scrap metal waste generation, and dampens acoustic noise pollution in the lab or workshop
GreenComp competences involved:
x Systems thinking x Problem solving x Collaboration x Critical thinking x Responsibility

## Slide 11
Activity: Project Planning Time for students: 45 min
Task | Responsible person | Deadline
Problem analysis | Patryk Januś | 23.05.2026
Sensor selection | Patryk Reiter | 23.05.2026
DAQ setup, measurement and analysis service in C# | Patryk Januś | 01.06.2026
Web Api backend, database integration | Patryk Reiter | 01.06.2026
Hardware setup, Controlling CNC | Szymon Korzuch | 01.06.2026
Front end for displaying results, measurement configuration | Natalia Szymeczko | 17.06.2026
Result analysis | Natalia Szymeczko | 20.06.2026
Final presentation | Szymon Korzuch | 24.06.2026
Communication method:
☐ MS Teams x Messenger ☐ WhatsApp x Discord ☐ Other: __________

## Slide 12
Activity: Project Planning
Risk Analysis Time for students: included in 45 min block
Potential problem | Potential impact | Solution
Sensor / DAQ communication drop | Missing threshold trigger events; no data sent to C# backend. | Implement connection retry logic and status indicators on the frontend.
Unstable signals / high noise | False software triggers or completely masked FFT resonance peaks. | Secure the accelerometer cable tightly; apply a software threshold band filter.
Insufficient measurement data | Captured time window is too short to calculate accurate decay rates. | Allow users to adjust pre-/post-trigger windows via frontend configs.
Time management issues | Missing project deadlines due to complex integration bugs. | Focus on early parallel development, so we have enough time to deal with any problems.
Example risks:
sensor malfunction,
DAQ communication problems,
unstable signals,
insufficient measurement data,
time management issues.

## Slide 13
Expected Deliverables Time for students: included in 45 min block
Our team plans to prepare:
x Working measurement system ☐ LabVIEW application
x Web application written in C# + React x Experimental dataset x Sustainability analysis x Final presentation x Technical report
Milestones and Deliverables
Milestone 1: Deadline: 01.06.2026
Complete C# backend integration with NI-DAQmx .NET libraries to successfully stream continuous acceleration data and verify software-threshold triggering.
Milestone 2: Deadline: 08.06.2026
Implement file logging to TDMS and Excel formats, establish the SQLite metadata registry, and connect the Web Frontend to display real-time charts.
Milestone 3:Deadline: 25.06.2026
Conduct full laboratory impact experiments across different structural beam scenarios, populate the database, and compile the final engineering report.
Expected project result:
A fully automated, high-precision vibration measurement system featuring a C# backend that captures transient impact responses via an IEPE accelerometer. The system successfully logs raw data to TDMS, structural configurations to Excel, and metadata to an SQLite registry, allowing an interactive web application to dynamically visualize structural resonance frequencies and damping trends.

## Slide 14
Questions / Consultation Needs Time for students: 10 min
Technical questions:
What is the optimal mathematical approach to calculate the damping ratio ($\zeta$) or decay rate directly from the extracted pre- and post-trigger time snapshot?
Organizational questions:
How will our team split development tasks between the C# DAQ backend, Excel/SQLite data storage layers, and the web frontend app?
Equipment/components needed:
Sensor: PCB Piezotronics Model 601A02 ICP® Accelerometer
DAQ Hardware: National Instruments NI-9232 IEPE module & NI-9171 USB Chassis
Excitation: Hammer that will allow us to achieve short impact time, and roughly repeatable impact force
Structure: CNC machine, with a way of setting spindle RPM manually
Software Environments: PC/Laptop running Visual Studio (C# .NET), NI-DAQmx drivers, Excel, and an SQLite instance

## Slide 15
Meeting 1 Summary Time for students: last 15 min
Today we completed:
x Team formation x Problem definition x Initial concept ☐ Measurement planning ☐ Sustainability analysis ☐ Project planning
Next step before Meeting 2:
Before our next meeting, our team will configure the core C# background worker service to verify connection stability with the NI-DAQmx .NET drivers. We will map out the specific schema for the SQLite metadata database and the formatting structure for the Excel results reports. Additionally, we plan to draft a mock dataset representing a typical impact decay waveform to test our frontend chart visualization ahead of the physical laboratory assembly.
Our team will:
x prepare technical concept x select sensors x design measurement setup
x prepare initial measurement interface in C# x collect technical information x prepare experimental procedure