## Slide 1
Erasmus+ Program 2024 Cooperation partnerships in higher education - 2024-1-ES01-KA220-HED-000246733
Student-centered learning for ENVIronmental sustainability at Higher Education Institutions
Measurement Systems and Sustainability
Project Title: Experimental identification of resonance frequency in a Mechanical structure
Meeting on June 18th.: Final Measurements, Data Analysis and Project Optimization
Team name:
Vibe Finders
Team members:
Patryk Januś Natalia Szymeczko
Patryk Reiter
Szymon Korzuch

## Slide 2
Progress Review (Time: 10 min)
What has been completed before Meeting 3?
x Working prototype ready x Prototype partially working x DAQ configured x Acquisition Software ready x Sensors calibrated x Preliminary measurements completed ☐ Problems still to solve: __________________

## Slide 3
Final Measurement Planning (Time: 20 min)
Is the system ready for final measurements?
Element | Status | Comments
Sensors | x OK / ☐ Problem | 
DAQ connection | x OK / ☐ Problem | 
Acquisition application | x OK / ☐ Problem | 
Data logging | x OK / ☐ Problem | 
Power supply / connections | ☐ OK / x Problem | Sometimes the connection with CNC machine gets lost especially during spindle spin-up, likely due to EMI interferences. After exchanging the cable for a different one we did not encounter this problem anymore
Experimental setup | x OK / ☐ Problem | 

## Slide 4
Final Measurement Planning (Time: included in 20 min)
Measurement objective:
To empirically identify the natural/resonance frequencies and damping behavior of a CNC machine structure across different table configurations, and to evaluate how these structural characteristics influence vibration levels during active operational conditions.
Test scenarios:
1. Hammer Impact Test: Impact the machine bed across different table positions (Front, Center, Back) to find natural frequencies and damping ratios.
2. Spindle Operational Test : Run the spindle at designated operational speeds to observe steady-state vibration and resonance amplification. In this experiment we wanted to select the spindle speed, such so we can observe what happens when the vibrations caused by the spindle allign with the dominant structural modes.

## Slide 5
Laboratory Measurements (Time: 60 min)
Measurement Log
Series | Test conditions | File name | Comments
1 | Hammer impact – bed in the back |  | For each hammer impact we repeated the measurement 3 times to verify the repeatability of the experiment
2 | Hammer impact – bed in the center |  | 
3 | Hammer impact – bed in the front |  | 
4 | Spindle Response – bed in the back |  | The actual spindle RPM (set to 12500RPM) did not allign well with structural modes determined during hammer impact testing, therefore for the next measurements we lowered it
5 | Spindle Response – bed in the back |  | spindle RPM set to 7500
6 | Spindle Response – bed in the center |  | spindle RPM set to 7500
7 | Spindle Response – bed in the front |  | spindle RPM set to 7500

## Slide 6
Data Quality Assessment (Time: 20 min)
Signal quality:
x Excellent ☐ Good ☐ Acceptable ☐ Poor — measurements must be repeated
Possible sources of errors:
☐ Sensor accuracy ☐ Calibration error ☐ Noise ☐ DAQ limitations ☐ Experimental setup x Human error – impossible to apply the same excitation strength each time for impact testing x Other: spindle RPM differing slightly from set values
Are the results reliable enough for the final report?
x Yes ☐ Partially ☐ No — additional measurements are needed
Justification:
Signal integrity was successfully maintained via low-impedance ICP/IEPE sensors, raw waveforms were cleanly captured without signal anomalies or clipping. Regression quality metrics (R^2) for the modal decay estimation were very high – for the dominant modes ranging between 0.978 and 0.994

## Slide 7
First Analysis of Results (Time: 25 min): Hammer impact tests
Main observations:
Very good signal quality and low noise visible
Some frequency components decay faster than others

## Slide 8
First Analysis of Results (Time: 25 min): Hammer impact tests
Main observations:
For each bed position the dominant frequenct appears to lie in the same band.
Because we used non-calibrated excitation method we cannot directly compare the amplitudes from this FFT plot

## Slide 9
Main observations:
After normalization its clearly visible, that the bed position affects the frequency of the dominant mode (it varies from ~350Hz for the fornt position to ~375Hz for the back positon
First Analysis of Results (Time: 25 min): Hammer impact tests

## Slide 10
Combined experiment results taken from the reports generated by our software
Main observations:
Regression quality is very good for most dominant modes at each bed position, indicating that the estimated daming rates are usable for further analysis
First Analysis of Results (Time: 25 min): Hammer impact tests

## Slide 11
After averaging the damping ratios of the dominant frequency accross each measurement per test configuration and computing the A type uncertainty and the expanded uncertainty we got the following results:
Main observations:
The dominant mode has the lowest frequency for the center position, and highest for the back position
The damping ratio is considerably smaller for this dominant mode with bed in the back position in comparison to the rest
First Analysis of Results (Time: 25 min): Hammer impact tests

## Slide 12
Main observations:
The dominant mode has the lowest frequency for the center position, and highest for the back position
The damping ratio is considerably smaller for this dominant mode with bed in the back position in comparison to the rest
First Analysis of Results (Time: 25 min): Forced excitation tests

## Slide 13
Sustainability Impact (Time: 15 min)
How can your system support sustainability?
x Reduced energy consumption ☐ Reduced water consumption ☐ Reduced waste x Extended equipment lifetime x Predictive maintenance x Improved efficiency x Reduced failures or losses
Evidence from measurements:
Hammer tests showed the back position has a low damping ratio (around 0.0123), meaning structural modes in this zone decay slowly. Spindle operation at 7,500 RPM generated a strong higher harmonic that aligned directly with this structural mode, concentrating more energy into that higher-frequency mode than the fundamental.
Sustainability recommendation:
Program the CNC spindle control system to dynamically bypass the 7,500 RPM speed setpoint when operating in the back position, preventing harmonic alignment with the high-energy structural mode.

## Slide 14
Preparation for Final Defence (Time: 20 min)
Final Report and Presentation
Final report sections to complete:
☐ Problem description ☐ System architecture ☐ Sensor selection and calibration ☐ DAQ configuration ☐ LabVIEW application ☐ Measurement procedure ☐ Results and analysis ☐ Sustainability evaluation ☐ Conclusions and recommendations
☐ Individual contribution of team members
Final presentation structure:
Problem and project objective
Measurement system
Experimental setup
Results
Sustainability impact
Conclusions
Individual contribution of team members

## Slide 15
Preparation for Final Defence (Time: included in 20 min)
Individual contribution of team members
Team member | Main responsibilities
Student 1 | [e.g. team coordination / measurements / documentation]
Student 2 | [e.g. sensor selection / calibration / experimental setup]
Student 3 | [e.g. DAQ configuration / LabVIEW development]
Student 4 | [e.g. data analysis / sustainability analysis / presentation]

## Slide 16
Task | Responsible person | Deadline
Complete measurements | - | -
Prepare graphs | Patryk Januś | 20.06.2026
Describe Acquisition application | Patryk Reiter | 20.06.2026
Write sustainability analysis | Szymon Korzuch | 22.06.2026
Prepare final report | All | 23.06.2026
Prepare final presentation | Natalia Szymeczko | 24.06.2026
Check files and attachments | Patryk Januś | 24.06.2026
Tasks Before Meeting 4 (Time: 15 min)